## Slide 1: Bridging the Gap Engineering
BRANDON ADAMS
MICHAEL ASHWORTH
ZACH CUMM
BRANDON DIAL
NATASHA NAPIER
JOHN SKAGGS

## Slide 2: Alternatives Summary
Comparison Criteria
  Cost
    Construction
    Material
  Shipping Limitations
    100 feet shipping limit
  Scheduling
  Manufacturing Availability
  Capacity Requirements
Alternatives
  Steel Plate Girder
  AASHTO Type V Concrete I-Beam
  Steel Rolled Beam

## Slide 3: Design Alt. #1
Steel Plate Girder
  AASHTO M 270 (ASTM 709M) – Grade 50 Steel
    Fy = 50 ksi
    Fu = 65 ksi
  4 plate girders
    9.0 feet spacing (center-to-center)
    2 ft – 10 in deck overhang
    18 in x 20 in x 5.875 in elastomeric bearing pad (e-Span 140)

## Slide 4: Design Alt. #1
Steel Plate Girder
  Spliced at L = 100’ and L = 25’
    AASHTO M 164 Type 3 Bolts
      7/8 in diameter
      328 bolts/beam x 4 beams = 1312 bolts total

## Slide 5: Plans
Steel Plate Girder Bridge Section

## Slide 6: Plans
Steel Plate Girder Detail - Section

## Slide 7: Plans
Connection Detail – Steel Alternatives

## Slide 8: Design Alt. #2
AASHTO Type V Concrete I-Beam
  4 girders
    8.0 feet spacing (center-to-center)
    125 feet span length
*Due to shipping limitations the concrete I-beam is not a feasible alternative.

## Slide 9: Design Alt. #3
Rolled Steel Beam (W Shape)
  W40x593
    4 Beams
      9’ spacing
      34” overhang
  593lbs per foot.
    Total weight = 148.5 tons
  *The total weight of the rolled beam is greater than the plate girder. The rolled steel beam is a more expensive alternative.

## Slide 10: Cost Assumptions
  Excludes any features that have a consistent design & cost (deck, parapet wall, etc.)
  Crane size calculated using an online crane calculator based off of weight and radius required.
  Running percent of 15% on job office overhead (Primary Contractor), 15% on home office overhead (Primary Contractor), 10% on Profit (Primary Contractor), 2% on bond (Primary Contractor), and 6% on taxes (Project). 25% running percent for sub-contractor.
  MII & RSMeans cost books used for any pricing that is not separately noted.
  10% of girder cost estimated for shipping

## Slide 11: Cost Comparison
Cost Comparison of Alternatives |  |  | 
Alternative | Direct Material Cost | Project Cost | Direct Cost
Steel Plate Girders | $215,000 | $445,000 | $295,000
AASHTO Type V Concrete I-Beam | $225,000 | $500,000 | $330,000
Steel Rolled Beam | $231,000 | $511,0o0 | $339,000
Steel Plate Girder Alternative was determined to be the cheapest with the next closest being 12% higher in cost
Difference between Steel Plate Girder and Rolled Steel Girder is significant enough ($45,000) to deem the Steel Plate Girder as a better choice from a cost perspective.

## Slide 12: Alternative Selection
Selected Alternative:
  Alternative #1 - Steel Plate Girder
  Justification for Alternative #1:
    Shipping length made the AASHTO Type V Beam Concrete I-Beams not feasible
    Cost of the Rolled Beam alternative compared to the Plate Girder alternative was too high

## Slide 13: Beam Optimizations
Calculated deflection limit
  1.875”
Flange changes required
  Top flange thickness increased from ¾” to 1 ½”
  Bottom flange thickness increased from 1 ¼” to 1 ¾”
New optimized deflection
  1.731”

## Slide 14: Design Capacity
Design capacity
  Ultimate Moment
    10,215.625 foot-kips
  Ultimate Shear
    335.09 kips
  Plastic moment (AASHTO Table D6.1-1)
    10,924.141 foot-kips
  Nominal moment (AASHTO 6.10.7.1.2)
    10,601.84 foot-kips
  Nominal moment > Ultimate moment
    Moment Capacity Performance Ratio of 96%

## Slide 15: Design Calculations
Shear capacity
  Longitudinal stiffener required 55 inches from abutment
  Nominal shear (AASHTO 6.10.9.3.2-2)
    479.336 kips
  Nominal Shear > Ultimate Shear
    Shear capacity is adequate

## Slide 16: Final Design
Final design contains
  Four steel plate girders
  Reinforced concrete deck
  Diaphragms
  Shear studs
  Parapet wlls
  Elastomeric bearings

## Slide 17: Final Design
Steel Plate Girder – AASHTO M 270 (ASTM 709M)
  Grade 50 steel
  Top Flange
    16”x 1 ½”
  Web
    55” x ½”
  Bottom Flange
    16” x 1 ¾”
Girder spacing
  9 feet center to center

## Slide 18: Final Design
Longitudinal stiffener
  ½” thick
  4 ½” wide
  55” deep
  Located 55” from abutment
Shear studs
  50 studs every 9”
  Transition to 12” spacing
Diaphragms
  W30 x 90
  31.25 feet apart

## Slide 19: Final Design
Elastomeric bearing pads
  18” x 20” x 5.875”
  1/8” thick internal steel plates
Bridge Deck
  8” thick reinforced concrete deck
  ¼” integral wearing surface
  Total deck thickness of 8 ¼”
  Compressive strength of 4 ksi
  Reinforced with #5 steel reinforcing bars
Parapets
  WVDOT Type F barrier
  Minimum height of 32”

## Slide 20: Plate Girder Costs
Steel Plate Girders: grade 50, 125’ long $343,669
Steel Plate Girder Installation $102,817
Shipping for Steel Plate Girder $35,483
Steel Plate Girder Misc. $34,573
( Bolts, Plates, stiffeners,
sheer studs, etc.)
Total Cost for Steel Plate Girders $516,542

## Slide 21: Final Costs
Class H concrete Deck:
Includes material, equipment, and labor $367,528
Deck:
Rebar including material and labor $22,447
Standard Type V Barrier:
Includes material, equipment, and labor $38,475
Elastomeric Bearing Pad:
5/8" T layers w/ 5.875" T total $12,648

## Slide 22: Final Costs
Concrete Class H Haunches: $16,158
Splice Connection Installation: $4,701
Crane- 40 Ton
Predicted Project Cost: $985,000

## Slide 23: Questions?